## Slide 1: Computerized Tomography
Deep Learning and Image Processing

## Slide 2: Computed Tomography (CT) Scan

## Slide 3: Principle
irradiate patient with X-rays from different directions
measure attenuations (absorption) of X-rays after passing through the body (different attenuations by different tissues)
use computer to reconstruct digital, cross-sectional images of the body interior, which are free from superpositions
move patient and repeat  3D image (stacking of 2D slices)
or anything else

## Slide 4
back projection

## Slide 5
with 32 back projections

## Slide 6: Tomographic Reconstruction
raw data from CT scan: multiple projections of the object (each projected point corresponds to superposition of specific direction)
in math terms: Radon transformation of the scanned structure
reconstruction: inverse Radon transformation (resulting in two-dimensional image  virtual slice)

## Slide 7
discrete Radon transform:
using normal representation of straight line

## Slide 8
sinogram:
Radon transform displayed as image

## Slide 9
back projections of the sinograms
single back projection (one direction):
final image by summing over all back projections:

## Slide 10: Filtered Back Projection
to reduce blurring effect: filter projections before back projection
need for high-pass filter
e.g., band-limited ramp filter using a Hamming windowing function:

## Slide 11: Fan-Beam Filtered Back Projection
so far looked at parallel beams
but modern CT systems use fan-beam geometry: need for many detectors
aliasing
decreasing angle increments (more detectors)

## Slide 12: Radiation Dose
need for low-dose method
image quality of filtered back projection susceptible to noise
but large dose increases needed to lower noise (inverse quadratic dependency)
iterative and model-based reconstruction can be used to reduce noise level (regularization)
but worse performance at low doses

## Slide 13: Deep Learning Reconstruction
idea: enhance noisy low-dose images to resemble high-dose ones
 ~30% lower radiation dose at same image quality
source

## Slide 14: Magnetic Resonance Imaging (MRI)
MRI uses magnetic fields and radio waves (instead of X-rays), applying nuclear magnetic resonance of hydrogen nuclei  no ionizing radiation
observed objects directly induce electrical signals (instead of X-ray absorption)  high resolutions possible
drawback: long scan times
deep learning reconstruction also used for MRI
 faster scans

## Slide 15: Other Deep Learning Applications
besides reconstruction, deep learning can also be used for:
classification and detection (e.g., tumors)
semantic segmentation (e.g., organs)
noise reduction and image enhancement
image registration and fusion across modalities (e.g., CT and MRI)
quantitative analysis
anomaly detection