## Slide 1: Computerized Tomography
Deep Learning and Image Processing

## Slide 2: Computed Tomography (CT) Scan

## Slide 3: Principle
irradiate patient with X-rays from different directions
measure attenuations (absorption) of X-rays after passing through the body (different attenuations by different tissues)
use computer to reconstruct digital, cross-sectional images of the body interior, which are free from superpositions
move patient and repeat  3D image (stacking of 2D slices)
or anything else

## Slide 4
back projection

## Slide 5
with 32 back projections

## Slide 6: Tomographic Reconstruction
raw data from CT scan: multiple projections of the object (each projected point corresponds to superposition of specific direction)
in math terms: Radon transformation of the scanned structure
reconstruction: inverse Radon transformation (resulting in two-dimensional image  virtual slice)

## Slide 7: Magnetic Resonance Imaging (MRI)
not only applicable for X-rays ...

## Slide 8
discrete Radon transform:
using normal representation of straight line

## Slide 9
sinogram:
Radon transform displayed as image

## Slide 10
back projections of the sinograms
single back projection (one direction):
final image by summing over all back projections:

## Slide 11: Filtered Back Projection
to reduce blurring effect: filter projections before back projection

## Slide 12: Fan-Beam Filtered Back Projection
so far looked at parallel beams
but modern CT systems use fan-beam geometry: need for many detectors
aliasing
decreasing angle increments (more detectors)

## Slide 13: Issues with Filtered Back Projection
...

## Slide 14: Iterative and Model-Based Reconstruction
...

## Slide 15: Deep Learning Reconstruction
…
~30% lower radiation dose at same image quality
also for MRI  faster acquisition